## Slide 1: How to Add Encryption to ATN
John Kelsey, Certicom, Dec 2001

## Slide 2: Overview of Presentation
Introduction and Requirements
Fitting Encryption into the System
Specifics of Encryption Mechanisms

## Slide 3: Introduction and Requirements
Goal: Add encryption support to ATN with minimal impact
Requirements
  Secure
  Little extra bandwidth used
  Flexible (w.r.t. national policies on crypto)
  Few changes to overall system

## Slide 4: Fitting it into the System: Overview
To fit encryption into system, we need to know how to:
  Request encryption
  Negotiate encryption mechanisms
  Derive keys
  Encrypt messages
  Use encryption with MACs/signatures
  Use encryption on ground-to-ground messages

## Slide 5: Fitting it into the System: Requesting Encryption
SecurityRequired variable:
  Additional values for requesting encryption
Same mechanism as requesting authentication in
  CM logon request
  CM contact request
  CM forward request
  Others? (CM server facility query)

## Slide 6: Fitting it into the System: Negotiating Enc. Mechanisms
Support many encryption mechanisms; need way to negotiate them.
Solution: Make ground CM responsible for deciding which mechanisms are used:
  Can use bandwidth to negotiate with ground entities.
  Can apply national policies w.r.t. cryptography

## Slide 7: Fitting it into the System: Negotiating Enc. Mechanisms (2)
Several possible ways for CM ground entity to decide:
  CM logon request contains list of up to 8 supported encryption mechanisms from aircraft
  CM can negotiate with ground entities for encryption mechanisms
  CM can look up preferences in table
  CM can check extended attributes of certificates (?)

## Slide 8: Fitting it into the System: Negotiating Enc. Mechanisms (3)
System works the same way regardless of how CM makes decision.
Need one default encryption mechanism, always supported.
Also need one default for "null encryption" to signal no encryption support.
All encryption mechanisms have no data expansion and acceptable level of security.

## Slide 9: Fitting it into the System: Negotiating Enc. Mechanisms (4)
CM-logon-response (and similar messages) contains indication of encryption mechanism for each application requested.
Adds one byte per application in bandwidth.
Total cost in bandwidth for encryption support is kept very low: 8 bytes + 1 byte per application requested.
Null encryption indicator byte signals no encryption support for that application.

## Slide 10: Fitting it into the System: Key Derivation
Reuse infrastructure for deriving MAC keys: K[e] for aircraft app W, ground app Y
KDF(Z;len;0x02||mech||W||Y||X||len)
  Z = static shared secret between aircraft and ground application entity Y.
  Mech = encryption mechanism negotiated
  W,Y = ID strings
  X = nonrepeating value for this CMA session
  Len = key length for this encryption mechanism

## Slide 11: Fitting it into the System: Key Derivation (2)
Z, X, W, and Y are all available from MAC key derivation
Len and mech are available from encryption mechanism negotiation

## Slide 12: Fitting it into the System: Encryption as an Abstract Fn.
Generic way to consider encryption
Encrypt(mech,key,count,sender,data)
  Mech from mechanism negotiation
  Key from key derivation
  Count, sender from current MAC computation
Rest of system doesn't care what mechanism is used or how it works

## Slide 13: Fitting it into the System: Order of Operations
Specific order of operations for this system:
  First, do any non-crypto processing to data, e.g., compression.
  Second, do encryption.
  Third, do MACing or signature
Reasons:
  Simplicity
  Easy resistance to reaction and chosen ciphertext attacks
  Can prove MAC/signature equally secure vs existential forgeries

## Slide 14: Fitting it into the System: Order of Operations(2)
Reaction Attacks:
  Send altered ciphertext and observe reaction
  Example: compression
Chosen Ciphertext Attacks
  Krazwyck's result from Crypto 2001
Signature forgery by changing keys/context
  Anderson/Needham result fro Crypto 1995
  No nonrepudiation needed here--signatures are for immediate use

## Slide 15: Fitting it into the System: Order of Operations (3)
Each message can be encrypted/decrypted in only one way, given counter and existing key and mechanism.
If you can forge signature/MAC because of encryption, you can find some signature/MAC forgeries using same attack
  See document mydraft1.txt for more details.

## Slide 16: Fitting it into the System: Ground-to-Ground Messages
Problem: G-G messages assume no context
Sender must know whether receiver can accept encrypted messages
  Extended attributes in certificates?
  Online database of ground entity preferences?

## Slide 17: Fitting it into the System: Ground-to-Ground Messages(2)
Sender makes header:
  Random number
  Sender ID
  Receiver ID
  Timestamp
Derives key (next slide)
Encrypts message under key (default mech.)
Signs ciphertext and sends

## Slide 18: Fitting it into the System: Ground-to-Ground Messages (3)
KDF(Z;len;0x02||mech||SID||RID||Rnd||len)
  Z = static shared secret from ECDH for sender and receiver
  Mech = default encryption mechanism
  SID, RID =sender ID, receiver ID
  Rnd = 128-bit random number from previous slide
  Len = length of key for this mechanism

## Slide 19: Summary So Far
We know how to:
  Request encryption
  Negotiate mechanism
  Derive keys
  Combine encryption, authentication, and other operations
  Encrypt ground-to-ground messages

## Slide 20: Encryption Mechanisms
Requirements
  Secure
  No data expansion
  Well-understood security properties
  Use of standard mechanisms wherever possible

## Slide 21: Encryption Mechanisms: Choosing Ciphers
Key lengths should be at least 100 bits.
  AES, 3DES, IDEA, Blowfish, RC4, etc.
Ciphers should be well-analyzed standards.
  AES, 3DES
No data expansion
  Block ciphers in CFB or OFB mode
  Variant modes (CBC with ciphertext stealing)
  Stream ciphers

## Slide 22: Encryption Mechanisms: Block Ciphers and Chaining Modes
Block ciphers are used in chaining modes.
Some standard modes (CFB,OFB) have no data expanison; these are the right ones for this system
Nonstandard modes available, but why use them?

## Slide 23: Encryption Mechanisms: Cipher Feedback (CFB)
Only encryption is used; faster for Rijndael/AES
Variable size feedback is possible; we use full block feedback.
No data expansion
Standard chaining mode
IV
M1
+
Ek
C1
+
Ek
C2
M2
+
Ek
C3
M3

## Slide 24: Encryption Mechanisms: CFB (2)
Suppose there are two equal ciphertext blocks with full-block CFB-mode, C[j]=C[k].
  C[j+1] = P[j+1] xor E(C[j])
  C[k+1] = P[k+1] xor E(C[k])
Solution: Change keys before internal collisions likely.
After 225 blocks enced with same key, prob of collision is low (about 1/32000).

## Slide 25: Encryption Mechanisms: Output Feedback (OFB)
Building a stream cipher with a block cipher
  Only encryption is used
  Feedback is independent of Data
Change Propagation -> NONE!
IV
M1
+
Ek
C1
+
Ek
C2
M2
+
Ek
C3
M3

## Slide 26: Encryption Mechanisms: OFB Mode Problems
IV1 == IV2 leads to identical keystream for two messages (easy to avoid)
IV1 = KS2 (collision with keystream block) leads to identical keystream (hard to avoid)
With 217 messages sent, prob of such a collision is very low (<1/1000000000).
But collision is much more dangerous--leaks about half of message, not just one block.

## Slide 27: Encryption Mechanisms: Choosing Block Ciphers
AES and 3DES are well understood
  Lots of public analysis
  Lots of experience analyzing block ciphers
  Lots of experience using block ciphers
Other block ciphers can be used
  Need at least 48 bit block
  Need at least 100 bit key

## Slide 28: Encryption Mechanisms: The Abstract Encryption Fn
Encrypt(mech;key;count;senderID;data)
Mechanisms must support this.
  Secure encryption
  Different count or sender changes message even if data is equal for two such messages.
  No expansion of data

## Slide 29: Encryption Mechanisms: Using Chaining Modes and IVs
Chaining modes (CFB,OFB) need IV s to be secure
IV = S||C||00..0
  S = 0x00 for aircraft-sent message, 0x01 for ground-sent message
  C = 16-bit counter (e.g., CountU,V.)
  00..0 = binary zero padding

## Slide 30: Encryption Mechanisms: Using Chaining Modes (2)
Why are these acceptable IV s?
  Requirement: IV s must never repeat for same key
  Counter and sender byte guarantee this
  No other requirements for IV s.

## Slide 31: Encryption Mechanisms: Recommended Mechanisms
AES-128-CFB
Two-key triple-DES-CFB
Recommend AES-128 as default.

## Slide 32: Encryption Mechanisms: Caveats
With triple-DES, if count of messages goes very high (e.g., 225), start expecting small leaks of plaintext.
These modes must be used with MACs or signatures; they provide no guarantee of authenticity.

## Slide 33: Encryption Mechanisms: Summary
We know how to make encryption mechanisms with all our required properties:
  Secure
  No data expansion
  Standards-based
We have recommended two specific mechanisms, AES-128-CFB and
3DES-112-CFB.